## Slide 1: INSTRUMENT CLUSTER
Presented By: Ayyali Anusha
Muskan
Naveen R
Spoorti V H
Sushil M K

## Slide 2
CONTENTS
1.INTRODUCTION
2.REQUIREMENTS
3.SYSTEM BLOCK DIAGRAM
4.HARDWARE BLOCK DIAGRAM
5.FUNCTIONAL BLOCK DIAGRAM
6.SEQUENTIAL FLOW CHART
7.TEST CASES
8.DATA BASE

## Slide 3
INTRODUCTION:
The Instrument Cluster of a vehicle is the dashboard where it deals the several parameters like Speed, fuel level, etc and switches are also located.
The vehicles Instrument Cluster located below the steering of the vehicle.
It gives the speed of the vehicle, the speed of the engine, how much fuel is remaining in the tank , the temperature of the engine and some other parameters.
The trip computer readout is mounted on the Instrument Cluster of the vehicle.

## Slide 4
REQUIREMENTS:
Instrument cluster output warning lamp shall be set ON when the cruise control CAN message is transmitted.
Instrument cluster output warning lamp shall be set OFF when the cruise control CAN message is missing .
Instrument cluster output warning lamp shall be set OFF when the occupant classification message is missing.
Instrument cluster output warning lamp shall be set ON when the occupant classification message is transmitted.

## Slide 5
SYSTEM BLOCK DIAGRAM:
INSTRUMENT
CLUSTER
(Processed data stored in memory)
Warning lamp status input from cruise control and occupant classification
1. Cruise Control warning lamp status.
2. Occupant Classification warning lamp status.
Trip switch reset
Faulty status if CC input CAN message is missing
H/W I/P
H/W O/P
CAN O/P
CAN I/P
H/W O/P
Faulty status if OC input CAN message is missing
SET or RESET
H/W O/P

## Slide 6
PIC18F458
Power supply (12 V)
Switch
LAMP 2(CC)
CAN Transceiver
LAMP 3(OC)
LAMP 1 (TS)
CAN Device (IXXAT)
HARDWARE BLOCK DIAGRAM:

## Slide 7
FUNCTIONAL BLOCK DIAGRAM:
Cruise Data
Occupant Data
CAN Receiver( )
Trip Switch
Transmit ( )
LED ON/OFF
Occupant
message id
PIC18F458
Cruise message id
Display
LED ON/OFF
Display
LED
RESET (0)
SET(1)
Interrupt( )

## Slide 8
SEQUENTIAL FLOW CHART:
Start
Stop
LED ON
Configure bits
System Initialization ( )
CAN Initialization ( )
Main()
While(1)
Buffer=0x04
SIDL/H=set
TXB0CON=0x08
If
Interrupt()
CAN read ( )
LED OFF
F
T
F

## Slide 9
Stop
Start
CAN Initialization Flow Chart:
Enable RB3
Disable RB2
Set CAN to configuration mode
While status != normal mode
Set Baud Rate
Check CAN i/o Registers
Set CAN to normal mode
F
T

## Slide 10
System Initialization Flow Chart:
Start
Enable Global Identifier(GIE)
Enable Peripheral Identifier(PEIE)
Stop

## Slide 11
Disable TRISC;
Disable RC7;
Disable LATC
if(RC7==0)
Start
Trip Switch Flow Chart:
SET LATC=1
LC7=0
Tx()
if
(RC7==1)
if (msg[3]==0x03)
If msg[3]==0x03)
Stop
F
T
T
Tx()
T
F
F
T

## Slide 12
System Initialization ( )
CAN Initialization ( )
Cruise ( )
Occupant ( )
Trip Switch()
Start
Main function Flow Chart:
stop

## Slide 13
Start
Set CAN to 0x0C
Array[]=Buffers
Set SIDL/SIDH
Set DLC
Set RXB0FUL=0x00
Stop
Receive Flow chart:

## Slide 14
Start
Set SIDL/SIDH
Set DLC
Set RXB0 to
Databyte1=0x03
Databyte3=0x03
Databyte5=0x04
Stop
Transmit Flow chart:

## Slide 15
Start
RXB0IF=0
receive
if RXB0IF
if (msg[3]==0x03)
Msg[1]==0x03
LATB =~ LATB
Stop
LATB =~ LATB
F
F
T
T
T
Interrupt Flow Chart:
F

## Slide 16
TC ID | TYPE | Pre condition | Test Case Name | Test Case Steps | Expected Result | Obtained Result
TC_CC_1 | Test Case | 1.ECU is powered ON 2.Fault free set up | Trip Switch | 1.Checking the Trip switch ON status. 2. Checking the Trip switch OFF status. | 1.Warning Lamp is activated to ON status. 2.Warning Lamp is activated to OFF status. | 1.Warning Lamp is activated to ON status. 2.Warning Lamp is activated to OFF status.
TC_CC_2 | Test Case | 1.ECU is powered ON 2.Fault free set up | Cruise Control | 1.Checking the obtained data from cruise message is not missing. 2.Checking the obtained data from cruise message is missing . | 1.Warning Lamp is activated to ON status. 2.Warning Lamp is activated to OFF status | 1.Warning Lamp is activated to ON status. 2.Warning Lamp is activated to OFF status
TC_CC_3 | Test Case | 1.ECU is powered ON 2.Fault free set up | Occupant classification | 1.Checking the obtained data from Occupant message is not missing. 2.Checking the obtained data from Occupant message is missing. | 1.Warning Lamp is activated to ON status. 2.Warning Lamp is activated to OFF status | 1.Warning Lamp is activated to ON status. 2.Warning Lamp is activated to OFF status
TEST CASES:

## Slide 17
Node Description | Node name | Message ID | Cycle Time (ms) | Message Size | Byte 7 | Byte 6 | Byte 5 | Byte 4 | Byte 3 | Byte 2 | Byte 1 | Byte 0
Instrument Cluster | IC | 0x88 | 1000 | 08 |  |  | Trip Switch status: Bit 2 Reset/ No Reset |  | Occupant Classification: Bit 0-Bit 1 |  | Warning Lamp activated/Faulty/not activated: Bit 0-Bit1 | 
DATA BASE: